## Slide 1: Reinforcement Learning to Enhance Spatial Reuse in Dense Wireless Networks
a Thesis Proposal

## Slide 2: Outline
Motivation
Spatial Reuse in Wireless Networks
Current SR Solutions for IEEE 802.11 WLANs
Reinforcement Learning for SR in IEEE 802.11ax
Research Activity
Future Work

## Slide 3: Motivation

## Slide 4: Next-generation IEEE 802.11 WLANs
Future WLAN deployments will be characterised by the high amount of devices that will coexist (e.g. 1 user/m2). The TGax provides a set of dense scenarios.
Residential
Enterprise
Indoor small BSS
Outdoor large BSS
Residential
+ Outdoor large BSS
Scenarios in IEEE 802.11ax
Topologies
Coordinated
Uncoordinated
Mixed
A central entity controls all the devices in the WN
Examples: University campus, offices
Independent WNs act autonomously
Examples: Residential buildings
Coordinated & uncoordinated deployments coexist
Examples: shopping mall

## Slide 5: Coexistence Issues in IEEE WLANs
Mainly produced by coexistence between devices operating at the same frequency band. Several mechanisms are provided in Time, Frequency and Space domains.
Weaknesses in the current distributed mechanisms
  Hidden/Exposed node problems
  Collisions by backoff
  …
Dense & chaotic scenarios
  Easiness of deployments
  Heterogeneous deployments
High bandwidth requirements
  Computational power moving to the cloud (more communication)
…
Root Causes
Potential Solutions
Time
Space
Frequency
Transmission Power Control (TPC)
Carrier Sense Threshold CST adjustment
Directional Transmissions
Interference cancellation
Scheduling
Contention Window (CW) adaptation
Dynamic Spectrum Access (DSA)
Dynamic Channel Bonding (DCB)
Space

## Slide 6: Challenges
Wireless channels are dynamic
  Network conditions
  Users activity
  Traffic patters
Wireless channels are shared
Strict QoS in many applications

## Slide 7: Moving into Artificial Intelligence
AI may satisfy the high-demanding requirements in next-generation scenarios. Upward trend in combining AI with Wireless Communications.
[2] Littman, M., & Boyan, J. (1993, July). A distributed reinforcement learning scheme for network routing. In Proceedings of the international workshop on applications of neural networks to telecommunications (pp. 45-51). Psychology Press.
[3] Bojovic, B., Baldo, N., Nin-Guerrero, J., & Dini, P. (2011, December). A supervised learning approach to cognitive access point selection. In GLOBECOM Workshops (GC Wkshps), 2011 IEEE (pp. 1100-1105). IEEE.
[4] Bojovic, B., Baldo, N., & Dini, P. (2012, January). A neural network based cognitive engine for IEEE 802.11 WLAN access point selection. In Consumer Communications and Networking Conference (CCNC), 2012 IEEE (pp. 864-868). IEEE.
[5] Combes, R., Proutiere, A., Yun, D., Ok, J., & Yi, Y. (2014, April). Optimal rate sampling in 802.11 systems. In INFOCOM, 2014 Proceedings IEEE (pp. 2760-2767). IEEE.
[6] Miozzo, M., Giupponi, L., Rossi, M., & Dini, P. (2015, June). Distributed Q-learning for energy harvesting Heterogeneous Networks. In Communication Workshop (ICCW), 2015 IEEE International Conference on (pp. 2006-2011). IEEE.
Previous Work
Packet routing [2]
Rate sampling [5]
AP selection [3, 4]
Q-learning
Multi-Armed Bandits
Neural Networks
Energy harvesting [6]
NP-complete
Variable environment
Fast-convergence must be granted
Why AI?
Problem
Solution
Observations-based learning process
Optimal solution approximation
Sensitive to modifications

## Slide 8: Motivation - Recap
Coexistence issues in WNs
Challenging next-generation scenarios
Moving into AI
Main causes: high-density, chaotic deployments, bandwidth-hungry applications…
Potential solutions: Time, Space and Frequency domains
1
1.1
1.2
1.3
2

## Slide 9: Spatial Reuse in Wireless Networks

## Slide 10: DCF in IEEE 802.11 WLANs
The Distributed Coordination Function (DCF) orchestrates the channel access for IEEE 802.11 devices in a decentralised way. It uses CSMA/CA and BEB.
Node 1 listens to Node 2
*Conditioned to a fixed CST
STA 1
STA 2
AP
Data range
Carrier sense range

## Slide 11: DCF in IEEE 802.11 WLANs
CSMA/CA is not optimal in dense environment. Leads to coexistence issues such as Hidden or Exposed terminal problems. The overall throughput is compromised.
Exposed Terminal Problem
Hidden Terminal Problem
Transmitters sense each other
Receivers are not affected by interferring nodes
The number of parallel transmissions decreases
Transmitters do not sense each other
Receivers are affected by interferring nodes
The collisions probability increases
EXAMPLE: AP2 and AP3 transmit to STA2 and STA3, respectively. However, both STA2 and STA3 listen to AP2 and AP3, so collisions may occur.
EXAMPLE: AP1 and AP2 can transmit to STA1 and STA2, respectively. However, only one AP can transmit at the same time.
Exposed Terminal Problem
STA 1
STA 2
AP 1
STA 3
AP 2
AP 3
Hidden Terminal Problem
*Conditioned to a fixed tx power / CST
Data range
Carrier sense range

## Slide 12: Ready-to-Send/Clear-to-Send (RTS/CTS)
RTS/CTS attempts to solve the collisions problem, but coexistence issues still appear in IEEE 802.11 WLANs
RTS/CTS does not solve the performance issues in CSMA/CA
Performance anomalies in case of existing asymetric links [1]
Hidden node problem still occurs
  RTS or CTS not heard
STA 1
STA 2
AP 1
AP 2
Data range
Carrier sense range
*Conditioned to a fixed tx power / CST

## Slide 13: Spatial Reuse
Directional Transmissions
Reduce the interference area
Increase the number of parallel transmissions
Omnidirectional transmission
Directional transmission
AP 1
STA 1
STA 1
AP 1
STA 1
AP 1
STA 1
AP 1
TPC
Decrease the transmission area
    Increase the number of parallel transmissions
Increase the transmission area
  Allow further transmissions
AP 2
Initial tx power
STA 2
STA 1
AP 1
Reduced tx power
Spatial reuse aims to increase the capacity in an area in which several devices share the medium.
CST adjustment
Reduce the carrier sense area
    Increase the number of parallel transmissions
Increase the carrier sense area
  Allow further transmissions
STA 1
AP 1
AP 2
Reduced CST to avoid AP3’s interference
Initial CST in which collisions occur
Interference cancellation
Increase the number of parallel transmissions
PHY overhead of training sequences
Antennas 1 and 2 transmit simultaneously to antennas 3 and 4, respectively.
Antenna 1
Antenna 3
Antenna 2
Antenna 4

## Slide 14: Effects on TPC and CST Adjustment
Adjusting either the power or the sensitivity has direct effects on the performance of a WLAN, specially in high-density scenarios.

## Slide 15: Dynamic Channel Allocation
Shared by many technologies (802.11, 802.15, U-LTE…)
2.4 and 5 GHz bands
Overlapping channels with co-channel interference
DCA aims to properly allocate the available frequency channels among the overlapping wireless devices. A proper DCA relaxes the SR problem.
STA 1
STA 2
AP 1
STA 3
AP 2
AP 3
STA 1
STA 2
AP 1
STA 3
AP 2
AP 3
Channel 1
Channel 2
Channel 3
Industrial, Scientific and Medical (ISM) band
Smart channel allocation helps at reducing the interference
The number of parallel transmissions is notably increased

## Slide 16: Spatial Reuse in WNs - Recap
In general, trade-off between idle periods and collisions
DCF shows poor performance in dense environments
Hidden and Exposed node problems
RTS/CTS aims to solve hidden node problem, but also has weaknesses
Tuning the transmit power and the CST implies several trade-offs
SR aims to increase the number of parallel transmissions in overlapping scenarios
SR depends the transmit power and the CST
Other advanced techniques help at SR enhancement
1
1.1
1.2
1.3
2
2.1
2.2
2.3

## Slide 17: Current SR Solutions for IEEE 802.11 WLANs

## Slide 18: Previous Work in TPC
Power Adaptation
Topology control
Per-packet based
Interference unaware
Interference aware
Busy Tone or Multiple Channel
Single Channel
Single Channel
Busy Tone or Multiple Channel
Single Channel

## Slide 19: Previous Work in TPC

## Slide 20: Previous Work in CST Adjustment
CST Adaptation
Uncoordinated
Coordinated
Centralised
Communication-based
DSC

## Slide 21: Previous Work in CST Adjustment

## Slide 22: Tranmit Power and CST Relationship

## Slide 23: Previous Work in DCA - Coordinated

## Slide 24: Previous Work in DCA - Unoordinated

## Slide 25: Reinforcement Learning for SR in IEEE 802.11ax

## Slide 27: RL in WNs – State-of-the-Art
Many categorizations: learner (passive/active), environment (known/unknown), model (with/without states)…
Prediction
Control
* Direct methods (estimate
the optimal action-values directly)
* Actor- critic methods
based on direct policy improvement and policy gradient
+ optimizing online performance (bandit problems and MDPs)
+ methods that aim at developing methods that can be used in large-scale applications
+ tabular (Monte-Carlo and TD(λ))
+ Function approximation (large states space)
* gradient descend (GTD2 and TDC)
* least-squares methods (LSTD(λ) and λ-LSPE)

## Slide 28: RL in WNs – Feasibility & Considerations

## Slide 29: Research Activity

## Slide 30: Expected Contributions
Understand challenges & limitations in future WLANs
Study the practicality of using RL to enhance SR in WNs
Design decentralised ML-based solutions for enhancing SR
Provide centralised ML-based solutions for enhancing SR
Integrate these solutions with others, such as DCB
1
2
3.1
3.2
4

## Slide 31: Analytical Models & Simulation Tools
Tools: CTMN, Komondor, ns-3…

## Slide 32: Ongoing work
Understanding the challenges and limitations in future WLANs, thus allowing researchers to deeply understand the topic and provide new solutions. To do so, we aim to perform an exhaustive analysis of the state-of-the-art in spatial reuse, as well as in the usage of Artificial Intelligence (AI) in WNs.
Exploring the feasibility of applying AI techniques to enhance spatial reuse in WNs, i.e., studying its practicality to show if they allow improving the performance of a given WN. In addition, we aim to show the benefits and limitations of applying a set of techniques for different architectures (e.g., fully centralised, uncoordinated, etc.). Regarding the network architecture, it is important to deeply analyse in which devices must a candidate solution be implemented, as well as in which of the protocols layer (e.g., PHY, MAC, Network, etc.). For the latter, the decision must be done according to the available input information in each level and the impact on the network performance.
Designing decentralised ML-based solutions for enhancing spatial reuse, so that WNs become autonomous systems through self-configuration. Moreover, it is also of importance to provide real-time mechanisms that can satisfy the challenge that variability in WNs supposes. We aim to explore both coordinated and uncoordinated approaches, motivated by the chaotic scenarios in which several independent WNs coexist (e.g., residential buildings).
As an extension of the previous point, we also aim to provide centralised ML-based solutions, so that many other fully controlled scenarios (e.g., university campus, airport, etc.) are covered. In such environments, it is important to analyse the trade-off between the optimality of the solution and the required time to achieve it.
Integrating the abovementioned solutions with others, such as Dynamic Channel Bonding, to provide a higher improvement in WNs performance.

## Slide 33: Future Work

## Slide 35: Reinforcement Learning to Enhance Spatial Reuse in Dense Wireless Networks

## Slide 36: References
[2] Littman, M., & Boyan, J. (1993, July). A distributed reinforcement learning scheme for network routing. In Proceedings of the international workshop on applications of neural networks to telecommunications (pp. 45-51). Psychology Press.
[3] Bojovic, B., Baldo, N., Nin-Guerrero, J., & Dini, P. (2011, December). A supervised learning approach to cognitive access point selection. In GLOBECOM Workshops (GC Wkshps), 2011 IEEE (pp. 1100-1105). IEEE.
[4] Bojovic, B., Baldo, N., & Dini, P. (2012, January). A neural network based cognitive engine for IEEE 802.11 WLAN access point selection. In Consumer Communications and Networking Conference (CCNC), 2012 IEEE (pp. 864-868). IEEE.
[5] Combes, R., Proutiere, A., Yun, D., Ok, J., & Yi, Y. (2014, April). Optimal rate sampling in 802.11 systems. In INFOCOM, 2014 Proceedings IEEE (pp. 2760-2767). IEEE.
[6] Miozzo, M., Giupponi, L., Rossi, M., & Dini, P. (2015, June). Distributed Q-learning for energy harvesting Heterogeneous Networks. In Communication Workshop (ICCW), 2015 IEEE International Conference on (pp. 2006-2011). IEEE.
[1] Sobrinho, J. L., De Haan, R., & Brazio, J. M. (2005, March). Why RTS-CTS is not your ideal wireless LAN multiple access protocol. In Wireless Communications and Networking Conference, 2005 IEEE (Vol. 1, pp. 81-87). IEEE.
[7] Wilhelmi, F., Bellalta, B., Cano, C., & Jonsson, A. (2017). Implications of Decentralized Q-learning Resource Allocation in Wireless Networks. arXiv preprint arXiv:1705.10508.